## Slide 1: Time-Lapse Seismic Monitoring
Guy Drijkoningen

## Slide 2
Course contents
Time-lapse seismic monitoring : why ?
Some basic principles
Some examples
Rock-physics models
(exercise on fluid substitution and forward modelling)
4D seismic data processing
4D interpretation convention and standards
(exercise on base and two monitor data sets Sleipner)

## Slide 3
Collection of slides from many sources
Rodney Calvert (Shell) 2005 EAGE DISC course
Some of Peter Mesdag (previously CGG) and Rob Arts (TNO) slides
Paul Hatchell (Shell) 2018 SEG DISC course
Some of Paul Zwartjes’ (when at Shell) projects

## Slide 4
Insights and Methods for
4D Reservoir Monitoring
and Characterization
by Rodney Calvert
Oct, 2005

## Slide 5: Time-Lapse Seismic Monitoring
4D = repeatable 3D
= differences in 3D
(+ possible update well/production information)
Monitoring is measuring production-related changes through time to better understand and manage our reservoirs.
Time-Lapse is measuring changes through time
1D, 2D or 3D. Survey over times of days, weeks, …
(not within seismic 3D window, e.g. 6 s)

## Slide 6: Why Time-Lapse Seismic Monitoring?
Monitoring processes:
- oil- and gas-production
- CO2 storage
- geothermal flow
- changes in the shallow subsurface
- …
Mainly processes taking on a scale of days, weeks, …,
years – typical in engineering
(geological time scales: usually not captured)

## Slide 7
Production technology ?
injector
producer
We cannot see what we are doing.
We would like to administer our care more precisely.
To do this we have to learn the anatomy and circulation system of our reservoir and surrounding rocks.
(from Stichting DAP)

## Slide 8
Reservoir anatomy

## Slide 9
Reservoir heterogeneity at all scales controls permeability
Figure 2-7
Page 13

## Slide 10
Premise

## Slide 11
If we are going to manage supply then we will have to monitor our fields beyond the wells
We cannot reliably predict 3D heterogeneity.
Premise
or
?

## Slide 12
base
monitor
difference ?
Differences may be simpler than the original
(Zwartjes 2019)

## Slide 13
A reservoir is never simpler than at the start
we have only one chance to get it right !

## Slide 14
Some lessons
We cannot predict reservoir flow; we must observe it.
Geophysicists must work with others to make this a success.
With care we can repeat most seismic “noise”.
We can get good 4D results with single-fold data.
Why are there good 4D results in the North Sea where seismic is poor and few in Gulf of Mexico where seismic is good?
3D makes a static picture, 4D examines living change.

## Slide 15: Some basic principles

## Slide 16: Signal Analysis in 4D
Small time shift
gives large change
in amplitude difference
Differencing seismic data a sensitive process!

## Slide 17: Measure often used

## Slide 18: Measure often used

## Slide 19
Signal a(t) = A sin(w t)
Give it a small shift in time (Dt):
a(t+Dt) = A sin( w (t+Dt) )
Then difference (for small time shift) :
a(t+Dt) - a(t) = A cos(w t) w Dt
So then NRMS-difference:

## Slide 20
Typical values of NRMS-difference for small time shift Dt :
Dt = 1 ms at f = 50 Hz: RNRMS = 0.31
Dt = 0.1 ms at f = 50 Hz: RNRMS = 0.031
Dt = 0.01 ms at f = 50 Hz: RNRMS = 0.0031

## Slide 21
Amplitude change

## Slide 22
Signal a(t)
Give it a small amplitude change :
(1+DA) a(t)
Then difference:
DA a(t)
So then NRMS-difference:
RNRMS = DA

## Slide 23: Measures …
Not sensitive to: static(time-shift) or phase;
Sensitive to: noise and changes in reflectivity (amplitude)

## Slide 24
Changes in velocity and mass density in layer
due to, e.g., CO2 or H2 storage
state 0
state 1
state 0
state 1
state 0
state 1
change in velocity
change in mass density
change in impedance

## Slide 25
(reflections for state 1) - (reflections for state 0) = difference response
Change in impedance contrast only,
change in amplitude only,
 shape the same
Change in impedance contrast + change in travel time,
Change in amplitude and change in shape

## Slide 26
r1
V1
t
r2
V2
d
t
production
d
A
4D seismic amplitude and timing changes with production
Sensitivity depends upon repeatability.
The Geophysics of seismic 4D
survey1
survey 2
oil
water
Figure 1-1
Page 2

## Slide 27
base
monitor
Difference
(monitor – base)
reflectivity
impedance
Difference traces identify the change.

## Slide 28
4D at work
some examples
Seeing is believing.

## Slide 29: 4D effects due to fluid changes

## Slide 30
(Calvert 2005)

## Slide 31: Time-lapse seismic monitoring: Seismic survey over same target over time
(From: TNO)
Courtesy EC_CO2STORE project
Offshore field Sleipner: CO2 injection
(From: BGS)

## Slide 32
Injection point
4D ability to monitor fluids moving in the subsurface
Figure 1-2
Page 3

## Slide 33
acoustic
impedance
water saturation
gas filled
oil filled
water filled
0 0.2 0.4 0.6 0.8 1.0
What do we mean when we say 30% saturation ?
Figure 3-7
Page 34

## Slide 34: 4D effects due to stress changes

## Slide 35
effective stress
velocity
P
P
P
effective stress = total stress - P
fluid pressure
Reservoir Pressure vs Velocity relationship
reduced pressure
increasing effective stress
increasing stiffness
increasing velocity
Figure 2-21
Page 24

## Slide 36: Injection Well Monitoring
The Many Faces of Pressure Changes in 4D Seismic at the Svale Field and Its Implication on Reservoir Management T. Alsos, B. Osdal & A. Høiås (StatoilHydro), EAGE 2009 Y004
“After 9 months of injection”
Notes: Well started injection at the end of 2005, survey acquired in 2006

## Slide 37
Stress arching – used by the Romans, now by 4D
On depletion the reservoir becomes less load bearing and the stress is taken up by the surrounds giving increased loading at the edges of the reservoir and increased horizontal and decreased vertical stress above.
Figure 3-11
Page 39

## Slide 38: Geomechanics and time strain

## Slide 39
Horizontal normal stress (MPa)
0.7
-0.7
100m thick 2x2 km rectangular reservoir buried at 1 km
Stress and strain for block-shaped reservoir
Vertical displacement (m)
0.025
-0.025
horizontal stress
vertical
displacement
Figure 3-12
Page 39

## Slide 40: Time shift and multiple layers

## Slide 41
Time shift from geomechanical model
Time shift between base and repeat
Time shift monitoring
(Courtesy the Mars Asset team and partners)

## Slide 42
What can we learn?
We can monitor fluid movements – of oil, gas and CO2.
We can measure pressure increase effects.
We can see unproduced reserves – and target them.
We can better place and control wells.
We can enable better reservoir simulations.
(production history matching is very non-unique)
Great value in seeing where changes are taking place

## Slide 43: From seismic data to rock-physics parameters
presentation based on material from Peter Mesdag (CGG) and Rob Arts (TNO)

## Slide 44: Biot-Gassman

## Slide 45: Poro-elastic wave equations (Biot):
where
u = displacement of solid
U = displacement of fluid
f = porosity
b0 = coefficient = viscosity*f2/permeability
P, Q, R = Biot coefficients
G = shear modulus
f, F = source terms
rf,s = fluid (f) and solid (s) density
rij = density-like terms:

## Slide 46: Low-frequency approximation of Biot equations
Assumptions (Rock Physics Handbook, Mavko et al., 1998):
  Low-frequency ( f << fc of rock with pores fc ~ 100 kHz to MHz)
  Rock is isotropic
  All minerals making up rock have same bulk and shear moduli
  Fluid-bearing rock is completely saturated
Gassmann:
  Low-frequency (where induced pore pressures equilibrated throughout pore space)
  Rock is statistically isotropic
  Homogeneous mineral modulus
where:

## Slide 47: Effect fluid change

## Slide 48: Gassman relations: fluid replacement
Equivalent forms:

## Slide 49: Effect porosity on other moduli and velocities

## Slide 50: Extension Gassman relations to include partial saturation
For partially saturated rocks at sufficiently low frequencies, an effective average modulus can be used for Kfl:
where S = saturation
Effect water saturation P- and S-wave velocities:

## Slide 51: Effect water saturation using Biot-Gassman equations
Effect water saturation on Vp of sand
(Bachrach & Nur, Geophysics, 1998)

## Slide 52: Typical values (although pressure/depth dependent)
Sandstones:
  Kmat = 36.9 GPa
  r = 2650 kg/m3
Shales:
  Kmat = 39.5 GPa
  r = 2700 kg/m3
Pore fluid:
  Kwater = 2.3 GPa
  Koil = 1.6 GPa
  Kgas = 0.03 GPa
  rwater = 1000 kg/m3
  roil = 850 kg/m3
  rgas = 130 kg/m3

## Slide 53: Property change as function of change in saturation

## Slide 54: Effect pressure change

## Slide 55: Effect of pressure changes
Granular models, Hertz:
where:
  Keff = effective bulk modulus
  C = average number of contacts per grain
  f = porosity
  G = shear modulus of grain material
  ν = Poisson ratio
  P = hydrostatic confining pressure
Granular models, Mindlin (using Hertz):
where Geff = effective shear modulus

## Slide 56: Effect of pressure changes: fitting model to core-versus-pressure data

## Slide 57: Change P-wave impedance as function of pressure (for different gas saturations)

## Slide 58: Change in S-wave impedance as function of pressure (for different gas saturations)

## Slide 59: Relating seismic changes (P- and S-impedance) to rock/fluid changes (pressure, saturation)

## Slide 60: Time-lapse impedance cross-plot: change in P-impedance vs. change in S-impedance

## Slide 61: change in P-impedance versus change in S-impedance

## Slide 62: Inversion (Landrø, 2001)
Reflection coefficient elastic media (1st order approximation):
Change in reflection coefficient due to fluid substitution (1st order approximation)
Change in reflection coefficient due to pore-pressure changes (1st order approximation)
Ratio’s Da/a and Db/b can be written in terms of pressure and saturation change, using empirical relationships (ki, li) :

## Slide 63: Inversion (Landrø, 2001)
Total change, due to pressure change and saturation change
This gives change in zero-angle reflection coefficient R0 and gradient G:
D R = D R0 + D G sin2θ
Two differences (D R0 and D G ) and two unknowns (DP and DS): solvable

## Slide 64
Amplitude changes at top reservoir (red) and traveltime changes at base reservoir (blue)
(from Landrø, 2001)
1985
1996

## Slide 65: Pressure and Saturation Inversion

## Slide 66: Pressure and Saturation Inversion

## Slide 67: Now: Exercise/Demo
Forward modelling time-lapse effect,
using fluid substitution

## Slide 68: (break)

## Slide 69: Causes of changes in time-lapse seismic monitoring
Many:
Differences in instrumentation
Differences in Geometry/positioning
Differences in “noise” characteristics:
Differences in processing
Differences in desired signal (reflections from the earth):
  velocity model
  reflectivity

## Slide 71: Causes of changes
Differences in instrumentation:
To be avoided !
I(t) = s(t) * r(t) * a(t)
where
I(t) = total instrumentation response
s(t) = source signal
r(t) = impulse response receiver
a(t) = impulse response of acquisition instrument
Any change in source, receiver or acquisition instrument will change
“effective wavelet” of seismogram, both in amplitude and phase.

## Slide 72: Causes of changes
Differences in Geometry/positioning
On land:
positioning can be made quite the same
However: old surveys may have different 3D design than new
ones
At sea:
same positioning difficult for streamers:
often data spatially resampled to same positions
fixed receivers on sea-water bottom (Ocean-Bottom Cables =
OBC’s)
source positioning dependent on boat sailing the same: also
difficult

## Slide 73: Causes of changes
Differences in “noise” characteristics:
Cultural noise, environmental noise, …
  On land:
  obvious that there are differences: stacking should be sufficient
  At sea:
  effect sea surface may have important effect on “effective wavelet”
Coupling characteristics (source, receiver)
  On land: deploying same source on same position may still give
  big difference
  Optimal: fixed receivers and fixed sources
Surface waves and refracted waves (on land):
    different due to changes in shallow subsurface

## Slide 74: Causes of changes
Differences in processing
No. of processing steps: at least 25 nowadays.
Many packages, many implementations…

## Slide 75: Causes of changes
Differences in processing
Important processing steps:
- geometry/positions
- wavelet extraction/deconvolution
- filtering (1D, 2D, 3D) noise
- surface-wave removal (mainly land issue)
- multiple-removal (mainly marine issue)
- NMO
- DMO (=Dip Move-Out)
- determination velocity model
- stacking data
- (first) time-migration
- iterative NMO/DMO/stack/migration (pre-stack/post-stack)
- calibration from well(s):
- update velocity model
- pre-stack time- or depth-migrations (if necessary)
- Impedance inversions
- Image-Processing final migrated images (attributes)

## Slide 76: 4D processing
Various stages of 4D processing.
The importance of QC in 4D processing.

## Slide 77: Balance 3D and 4D Considerations
4D
2 x the best 3D not necessarily the best for 4D
Noise
Resolution
Fold/Coverage
3D
Primary Preservation
Repeatability
Notes: Just as in acquisition, what appears the best for 3D is not necessarily the best for 4D. For example, harsh denoise on a 3D dataset may be deemed acceptable, but if the process attenuates the primary energy in any way, you will start to introduce 4D noise. Likewise, pushing the bandwidth on 3D may be useful to improve resolution, whereas in 4D we will see that higher frequencies are less repeatable and following the same approach, you might simply be lowering the signal to noise ratio without any benefit. You would have learned from the Geometric Repeatability module that repeatability relies on positioning of sources and receivers. In 3D processing, stacking as much data as possible is advantageous, whereas in 4D, stacking only repeatable data is better.

## Slide 78: Getting the Balance Wrong: 4D Takes No Prisoners!
‘Final’ 4D Difference
This is not 4D signal—below reservoir
Where is it coming from?
Notes: This is an example of how unforgiving 4D can be. The smiles seen on this 4D difference are not related to production but have been introduced by an overly data adaptive processing sequence.

## Slide 79: Why problem occurred
Extra pass of swell noise attenuation applied on one vintage due to high noise levels.
Attenuated of focused energy at synclines creates smiles on 4D difference of migrations later on.
Common Offset (CO) gathers after shot domain denoising
CO gather after shot and receiver domain denoising
Difference Pass 2 – Pass 1
Pass 1
Pass 2
Notes: An investigation traced the problem all the way back to the swell noise attenuation step. This was one of the first steps in the processing sequence but the noise wasn’t spotted until after the final migration when the signal to noise was improved. The problem occurred because an additional pass of swell noise attenuation in a different domain was applied to one of the datasets that was particularly noisy. The attenuation was too aggressive and removed some primary energy in a low frequency band along with the noise. Two key rules of 4D processing were breached in this example:
Preserve primaries at all costs (better to leave some noise in—it will likely stack out anyway)
Do the same to all vintages.

## Slide 80: Some Fundamental Rules of 4D Processing
  Referred to as Co-Processing or Dedicated 4D Processing
Process base and monitors together from scratch.
  Same pre-processing sequence and migration velocity model
Do the same to all vintages.
Select common data and throw away non-repeatable traces.
  Select reference survey to fix differences.
Use the extra dimension.
Use the best possible imaging for S/N.
Re-process old 4D regularly (<5 years) just like you would 3D.
1
2
3
4
5
6
Notes: Where possible, avoid comparing legacy datasets that have not been co-processed. The results are usually highly misleading. Even starting processing from archived pre-processed gathers is risky because the software versions might have changed between archived and new data and can you ever be 100% sure the archived data is processed exactly as it says in the report? Best to start from un-processed idented gathers or field data.

## Slide 81: The Absolute First Rule of 4D Processing
QC, QC and more QC
Notes: Attention to detail is everything in 4D processing as the smallest corrections or errors have a huge impact on the final result. You need to QC thoroughly with attributes and difference volumes right through the processing sequence. It is a false economy to go light on the QC—you will get burned!

## Slide 82: Using the extra dimension (4D Corrections)
Common instances where reference survey was used to fix differences related to acquisition conditions or errors.
Residual water column corrections (statics) in marine
Coupling or near surface differences on land or seabed
Positioning errors—small but significant systematic errors are common
Source wavelet — Global Matching
Repeatability differences — Local Matching

## Slide 83: Where Does 4D Noise Come From?
Need repeat ACQUISITION exactly OR perform perfect PROCESSING to correct for differences.
Shallow scatterers, small faults
Channels, reflector topography, (de)focusing, faults
Structural dips
Wavelength (m)
If these are captured in a migration velocity model, then at least timing is corrected.
Near surface usually disturbs wave front mostly due to steep diffraction curves, small Fresnel zones and large velocity contrasts in less compacted sediments.
Acquisition Differences
Heterogeneous Earth
=
4D Noise
Notes: This slide is animated. Click for each component to appear.
4D noise arises from the combination of an imperfect acquisition and a heterogeneous earth. To illustrate, look at the cartoon of two ray paths through a complex overburden. Although the subsurface reflection point is almost the same, small differences in source and receiver positions result in different propagation effects through the overburden, and ultimately a different recorded wavefield. For the perfect 4D survey, with no 4D noise, we therefore need an exact repeat of our baseline survey, or be able to correct for the differences in processing. In practice, we try and repeat our source and receiver positions as closely as possible with DEDICATED 4D surveys. The more heterogeneous the overburden, the more sensitive we are to positioning differences and the less likely that we can correct for them in processing. It is often the near surface that has the greatest impact on 4D data quality. Here, we have the most heterogeneity and it is challenging to capture it in our migration velocity models due to lack of offsets.

## Slide 84: Repeatability: Final Migrations Still Show Impact of Geometrical Repeatability
NRMS = 0.33
90-04
N
N
DS+DR = 72m
NRMS= 0.17
01-04
N
N
DS+DR = 31m
Smit and Brain 2006
NRMS = 0.26
98-04
N
N
DS+DR = 57m
Notes: This slide is animated. Click for the images on the right to appear.
Even after our processing is complete, we still see the impact of geometrical repeatability. Here we are comparing seismic repeatability, NRMS, at the top, against geometric repeatability, Delta source plus Delta receiver, at the bottom, for different 4D acquisitions from the Draugen field. We start by comparing the 2004 monitor to the pre-production 1990 survey. The 4D signal stands out in the main field area in red, but as the monitor was acquired with a different number of cables, the poor geometrical repeatability results in a reasonably high noise level. Next, we compare the 2004 to the 1998 survey. Here, the same number of cables were used, but the surveys were acquired as two separate 3D surveys without trying to repeat the source and receiver positions. The DSrc + DRcv has reduced as has the background 4D noise level. Finally, it is only when we look at the 2004 against the 2001 survey, do we see the benefits of truly dedicated 4D acquisition. Now, we have actively tried to repeat source and receiver positions, the noise level has dropped considerably and we can confidently interpret the small patches of 4D signal to the East.

## Slide 85: Repeatability Measures — NRMS
ARMS (base – mon)
½ (ARMS base + ARMS mon)
RRMS (=NRMS) = 100 * %
Positioning Differences
N/S
NRMS
RMS
Assuming good alignment/match and similar 4D noise, NRMS will reduce with increasing 3D amplitudes.
140
RMS Amplitude
RMS Amplitude
RMS Amplitude
Difference
Monitor
Base
Notes: This slide is animated. Click for the textbox and the image on the bottom half of the slide to appear.
Now, let us consider how we measure repeatability on seismic data. There are many different metrics, but the most commonly used in the industry is NRMS, Normalised RMS. NRMS is calculated from RMS amplitudes measured in a window. The RMS from the difference is normalised by the average of the base and monitor. In the case of good repeatability, there will be little 4D noise in the difference window and the NRMS will be low. In the course of a processing project, we might see the NRMS reduce from around 60% to under 20%. You can consider anything less than 20% to be good repeatability. Above 50%, noise levels are likely to mask even strong 4D signals. Note that window choice is important. Including 4D signal in the window will increase NRMS. It is also sensitive to 3D amplitudes due to the normalisation term. NRMS will reduce with increasing 3D RMS amplitudes if the 4D noise level is constant. We observe this relationship in the plot of NRMS against baseline RMS in the bottom right. NRMS will therefore vary across a survey if there a changes in 3D amplitudes, and so, be aware that geology as well as repeatability can impact NRMS.
Other attributes: Predictibility, CDR (BP) and SDR Total’s (Signal Distortion Ratio—Cantillo).

## Slide 86: Small time shifts cause large differences
Difference at 50 Hz for Dt = 1ms
-1.5
-1
-0.5
0
0.5
1
1.5
0
200
400
600
800
NRMS ≈ 2pf.Dt
1 ms shift @50 Hz NRMS = 31%
0.5 ms shift @25 Hz NRMS = 8%
0.1 ms shift @50 Hz NRMS = 3%
From Calvert DISC 2005
Repeatability decreases with increasing frequency.
Graph | Denotes
 | SIN(t)
 | SIN(t+dt)
 | Diff(with dt)
 | Diff(dt=0)
Notes: 4D seismic repeatability is very sensitive to time alignment. In this example, we take two sinusoids at 50 Hz and shift one of them by 1 ms. The dark purple curve is the difference between them. The NRMS in this case is 31%, which is equivalent to them being approximately 30% different in amplitude. Observe that the effect is frequency dependent and gets worse for higher frequencies. In processing, we try to solve for 4D statics in a number of ways, but most of our remaining 4D noise is related to small, localised timing differences that can be traced back to ray-path non-repeatability in acquisition.

## Slide 87: Using the Extra Dimension in a 4D Processing Flow
Base
Monitor 1
Monitor 2
Select common data
Noise Attenuation
Survey Specific Zero Phasing
Imaging
(common model)
4D Post Processing
Receiver Motion Correction
Apply tidal statics
4D corrections
Regularisation
Demultiple
Select common data
Select common data
Common offsets and record lengths
4D corrections
4D corrections
Use multiple datasets to solve for statics, navigation, amplitudes
Imaging
(common model)
Regularisation
Imaging
(common model)
Regularisation
Common Imaging
4D Post Processing
4D Post Processing
Residual matching and filtering
Noise Attenuation
Survey Specific Zero Phasing
Demultiple
Receiver Motion Correction
Apply tidal statics
Noise Attenuation
Survey Specific Zero Phasing
Receiver Motion Correction
Apply tidal statics
Demultiple
Common
pre-processing sequence
Notes: In this simplified marine processing flow, schematic we see that after a common pre-processing sequence, we compare all the vintages, and by selecting a reference, we can solve for the acquisition related differences between the surveys. For example, residual water velocity corrections. Note that because the pre-processing sequence is common, you can prepare existing surveys ahead of new 4D acquisition to reduce turnaround time (as long as they are still co-processed, that is, part of the same project). The migration velocity model may also be prepared in advance as we use a common model for all surveys. Note that during zero phasing it is better to process to a reference amplitude spectra so that the demultiple sequence behaves similarly for all vintages.

## Slide 88: Using the Extra Dimension in a 4D Processing Flow (cont)
Base
Monitor 1
Monitor 2
Select common data
Noise Attenuation
Survey Specific Zero Phasing
Imaging
(common model)
4D Post Processing
Receiver Motion Correction
Apply tidal statics
4D corrections
Regularisation
Demultiple
Select common data
Select common data
Common offsets and record lengths
4D corrections
4D corrections
Imaging
(common model)
Regularisation
Imaging
(common model)
Regularisation
Common Imaging
4D Post Processing
4D Post Processing
Noise Attenuation
Survey Specific Zero Phasing
Demultiple
Receiver Motion Correction
Apply tidal statics
Noise Attenuation
Survey Specific Zero Phasing
Receiver Motion Correction
Apply tidal statics
Demultiple
Common
pre-processing sequence
4D QC
4D QC
4D QC
4D QC
4D QC
4D QC
4D QC
4D QC
4D QC
4D QC
Notes: Thorough 4D QC should be performed at all major processing steps with particular care at the 4D corrections stage. We will see what kind of QC is involved in the next section.

## Slide 89: Example of a Data Correction Using Multiple Surveys
Global Match Filter
4D Difference
BCU
4D Difference with additional debubble
Residual bubble energy
Notes: In this case, after the pre-processing of a base and monitor, the 4D difference QC showed a low frequency artefact below the dominant reflector (BCU) in the section. By deriving a Global Match filter (all traces in survey compared), we were able to identify a wavelet difference that coincided with the bubble period of the baseline source. The source had been correctly modelled with the information at hand but the designature was clearly not removing the bubble energy as intended. However, by correlating the base and monitor surveys, we were able to derive a de-bubbling filter for the baseline. The 4D difference on the right shows that after application of this filter, the artefact is removed. In cases like these, we will also have improved the baseline data quality as the bubble noise is removed. 4D processing often results in improved 3D processing.

## Slide 90: 4D Processing Philosophy: Keep it Simple
Partially Data Adaptive:
Measure and correct for known physical effects (4D corrections)
Residual wavelet differences:
    Global match
Residual water column corrections:
    Sail line consistent 4D statics
    Water velocity statics
Reject non-repeatable traces with 4D Trace Selection (binning)
Navigation Errors (recorded positions incorrect)
Land surface consistent corrections
4D Demultiple
Processing Difficulty
Deterministic:
Correct for what we know
Zero phasing to account for:
    Source signature (+ directivity)
    Source + streamer depths
    Recording instruments
Streamer length differences
Tidal statics (heights predicted or measured)
Receiver Motion Correction—Correct for boat moving position while recording
Data Adaptive
Fix what is left by brute force
Local Matching
    Least Squares Filtering
    Neural Nets
    Geo-statistics
4D Trim statics
Time Alignment
...but only if you have to. Treat as a last resort.
Observe — Explain — Correct
Notes: The previous case is a good example of using multiple surveys to identify and fix inherent problems in our data. We have OBSERVED the effect on the 4D difference, EXPLAINED the origins of the effect and then were able to CORRECT the baseline survey. This approach is important as if we try and be too data adaptive, that is, force one dataset to look like another with local corrections, we are likely to damage our 4D signals and will probably introduce more noise on the final products. The key to good 4D processing is to keep it simple. First correct for what you know (DETERMINISTIC), then fix things in an acquisition consistent manner (PARTIALLY DATA ADAPTIVE) and only as a last resort or as an interpretation tool, apply LOCALLY ADAPTIVE data matching (also called warping).

## Slide 91: Recommended 4D QC Products
Intelligent 4D QC is THE key to a successful 4D Project.
Use these basics for quick and informative diagnosis.
4D Attribute Volumes
4D Differences
4D Attribute Maps
4D Matching Filters
Notes: As good 4D QC is the absolute first rule of 4D processing, you should be aware of how to do it. It is sadly true that QC can become a tick box exercise in generating attributes. If this is the case, you may as well not bother. Without the OBSERVE-EXPLAIN-CORRECT philosophy, important data issues and possible solutions will be missed and data quality will be compromised. It is also important to remember that attributes are very useful for finding and diagnosing problems but MUST be backed up with QC stack volumes and 4D differences, that is, looking at your data. This is where processor and interpreter can work together to identify signal and noise.

## Slide 92
4D Corrections
(mainly marine)

## Slide 93: The Cruel Sea: Water Column Corrections
Marine: acquisition on dynamic layer so need to consider:
Tides
  Water column thickness changes with tidal cycle
Water Velocities
  Seasonal changes and currents effect travel times
Ghosts
  Sea surface conditions change source depth and receiver ghosts
Noise
  Swell noise due to water turbulence
Multiples
  Extra passes through the variable water layer
Notes: This slide is animated. Click for the textbox to appear.
In marine 4D processing, the water column corrections are often the most significant corrections we make. The timing differences that result from different tidal heights (water column thickness) and variations in water velocity between the base and monitor will introduce significant 4D noise unless they are corrected. 4D difference sections are very sensitive to timing differences (especially the higher frequencies) and I would consider anything above 0.1ms worth trying to correct. At the limit of what we can correct are the differences in source depth due to wave height. With very accurate GPS and/or near field hydrophone recordings, it is possible to measure and correct wave heights on a shot by shot basis.
In addition to the timing differences, the state of the sea surface will also affect the source wavelet as the free surface receiver ghost will change. If the surface were flat calm, the ghost reflection coefficient would be −1 and the timing constant, but with wave disturbances, the reflection coefficient will reduce with scattering and the timing will change. In a series of papers, Ed Kragh of WesternGeco has shown that using continuous recording to extract very low frequencies, it is possible to create a sea surface model and correct the receiver ghost variations for more stable wavelets and reduced 4D noise. However, this is not a process that we routinely apply at the moment, but in acquisition, we do try and acquire in good conditions to minimise the variations.
Noise due to the pressure variations from wave motion (swell noise) must be dealt with as our surveys would be hugely expensive if we were only to acquire in perfect weather. In practice, we de-noise each survey independently but usually using the same parameters and while trying to ensure that we do not attenuate primaries in the process (see earlier).

## Slide 94: The Problem with Multiples
Not practical to acquire on same tide height
Primaries (P) corrected with water static and difference away
Multiples (M) have additional passes through water so primary static correction does not align them, resulting in 4D noise.
In deep water, measure water velocities (OBN processing)
Vm = Vb+ dV
tm = tb+dt
P
M
P
B M D (with water static)
dt
dt
2.dt
tidal diff
Notes: Unfortunately, it is not practical to acquire the same tidal height (we have tried!) as there are week to week variations and weather effects on the top of the regular tidal cycle. So, we must make the corrections in processing. Tidal height predictions are always available, and even better, if measured tides are recorded at a nearby platform as they will also include the weather effects. With these, we can make a simple static (timeshift) correction based on acquisition time. This is an 80% solution as even the measured tides are not perfectly accurate, are often extrapolated to the survey area and do not do anything for variations in water velocity. Therefore, we also use our actual data to correct the residuals.
Of course, these corrections are for primaries, but sea bed multiples will have additional passes through the water column and so require additional static corrections to be able to align. This is not practical, and so, we recognise that multiples will always be partially non-repeatable. The solution is simple—remove the multiples. Hence, a 4D sequence should try as hard as a 3D sequence to remove multiples because they will not subtract exactly. The additional constant is that you most definitely cannot attenuate any primary. See Calvert 4D Demultiple Method (DISC) for a novel solution.

## Slide 95: Water Column Corrections: No Statics Applied
4D Timeshifts Map
4D Timeshifts
Inline
2ms
-2ms
-5ms
multiplicity display
5ms
Measured tides
Predicted tides
Tidal corrections (microseconds) vs. time
Predicted tides do not account for atmospheric pressure, storm surges and so on
Errors generally within 0.3 ms (~20 cm)
1ms
4D Timeshifts Profile
Notes: Here are a series of 4D QC’s measuring 4D timeshifts (timing differences between 2 vintages) on a dataset prior to tidal corrections. The timeshifts are measured by cross-correlation in a long window and vary between +/− 2ms. They are displayed as a map (top) and as a profile (bottom). Note the N-S acquisition direction imprint: tides vary slowly relative to shooting speed, and so, there is little difference along a line. The variation is between lines which can be acquired days, weeks or even months apart. The profile display (plot timeshift against inline) clearly shows the line-to-line variations.
Note the difference in measured vs. predicted tides in this area in the top right display.

## Slide 96: Water Column Corrections: Tidal Statics Applied
4D Timeshifts
4D Timeshifts
2ms
-2ms
5ms
-5ms
Measured tides
Predicted tides
Tidal corrections (microseconds) vs. time
1ms
Still:
Predicted tides do not account for atmospheric pressure, storm surges and so on
Errors generally within 0.3ms (~20cm)
4D Timeshifts Map
Inline
multiplicity display
4D Timeshifts Profile
Notes: Now, we see the same QC’s after application of tidal statics. We see the striping significantly reduced, although, some are still present. This may be because the tidal measurements are not accurate or because we have other effects such as water velocity changes or cable or source depth variations.

## Slide 97: Water Column Corrections: Tidal Statics + 4D Statics
4D Timeshifts
4D Timeshifts
2ms
-2ms
5ms
-5ms
Correlate datasets and decompose timeshifts into sail lines and shotpoints. Take one correction per sail line or allow to vary smoothly (long lines)
Residuals from 0.3 to 0.1ms
Can do by cable, source either
4D Timeshift distributions
None
+ Tidal
+ 4D Statics
Sail line static corrections
4D Timeshifts Map
Inline
4D Timeshifts Profile
multiplicity display
Notes: The final step to correct the water column is to use one of our 4D datasets as a reference and align the other surveys to it. Note that if we try and align every trace independently (trim statics or warping) we run the risk of removing genuine 4D effects and is also noise sensitive. A better solution is to use statistics, knowing the tidal and velocity variations change slowly with time, to derive a single or slowly varying statics solution per sail line (sail line consistent statics). This robust solution has further corrected the timing variations. The profile is still not completely flat as the statics were derived in a different window using a limited offset range whereas this is an attribute measured on a full QC stack. Independent QC’s are vital to ensure a good solution. Note that you will need to exclude genuine production related timeshifts from the analysis.
The histograms show how the solution has improved through each of the steps.

## Slide 98: What is 4D Trace Selection (4D Binning)?
Variogram from seismic
NRMS
Dsrc + Drec
keep?
select
Base
Monitor
throw away
Drec
Dsrc
1 bin
Select only repeatable traces for further processing
Threshold
Reject
Ref: Brain 13. Multi-Vintage Binning
Notes: This slide is animated. Click for the different components of the images to appear.
With 4D trace selection, we wish to select only repeatable traces for further processing. You would have seen previously in the acquisition module that the source and receiver positioning is the major control on repeatability. We therefore select only traces with DSR less than a given threshold for further processing. In this example, we would probably keep the trace belonging to the orange star but would throw away the contribution from adjacent sail line. With a dedicated acquisition such as this, it is relatively easy to decide on the acceptance threshold but in cases with non-dedicated acquisition, for example, old pre-production baselines, we may need to either relax these criteria or select the best match per bin even if it is still not very repeatable. In the case of having multiple non-repeatable traces (and no repeatable ones) in a bin, it might be as well to keep all the traces regardless of repeatability as 4D noise will stack out to some extent.

## Slide 99: Trace Selection Example: Before Selection
Stack RRR after fold harmonisation
Dsrc + Drcvr from 2500m offset volume
Binning Criteria
1. Min Azimuth 2. Min offset
3. Nearest bin centre
Notes: In this example, we are comparing the seismic repeatability (RRR or NRMS) on the left with the difference in source plus difference in receiver positions (DSR) on a QC stack made after pre-processing (un-migrated). This survey was acquired with extra outer streamers to create an overlap at sail line boundaries, so in the case of differential feather between surveys, repeatable data is still acquired (see Geometric Repeatability pre-read). The seismic clearly shows non-repeatable stripes (yellow-red) where we have these overlaps (compare to DSR plot).

## Slide 100: Trace Selection Example: After Selection
Dsrc + Drcvr from 2500m offset volume
Stack RRR after 4D trace selection
Trace Selection
1. Min Dsource for 2002
Notes: Now, by applying 4D trace selection, we select only the monitor trace in these overlaps that matches the baseline. The DSR reduction on the right is matched by the NRMS reduction on the left.
Clearly, there are still some repeatability issues with this survey. For instance, the line on the far left was acquired in the wrong direction, as was the short infill line towards the centre and the undershoot of the platform was not repeated well. We now need to decide whether to remove the remaining non-repeatable data and interpolate or live with it. This is a typical 4D trace selection decision and depends on the size of the holes left to infill and the level of non-repeatability. Since this survey, we have managed to repeat the survey more accurately (including the undershoot) and have seen a corresponding improvement in 4D data quality.

## Slide 101: Trace Selection Example: Before Selection
4D Difference
Notes: This is the same example, but now we are looking at a crossline seismic 4D difference. Notice the banding of 4D noise at sail line boundaries.

## Slide 102: Trace Selection Example: After Selection
4D Difference
Notes: …and after the trace selection, much of the noise is removed.

## Slide 103: Causes of changes
Differences in processing (cont’d)
In next surveys, extra information often available from well(s) and production:
May be necessary to re-process original data !

## Slide 104: Causes of changes
Differences in desired signal (primary reflections from the earth):
  Velocity model
  Reflectivity image

## Slide 105: The Problem
4D Amplitude Change
4D Time Shift
Key questions:
Polarity?
Colour scale choice?
Attribute/window?
Key questions:
Polarity?
Reservoir timeshift or Overburden time shift?
Window?

## Slide 106: 4D Signal for Saturation Changes (Sweep)
OOWC
POWC
Impedance
OOWC
3D
Oil sand
Water sand
Shale
Shale
Produced
oil
OWC
rise
POWC
4D
Reflectivity
Notes: This Mickey mouse graph shows the effect of a HWC movement with resulting saturation changes in the produced interval.
  OOWC = Original OWC
  POWC = Present OWC
Irreducible oil saturation prevents complete displacement.
Where there was initially no reflection within the oil bearing interval, there is now a hard kick (oil on brine).
Where there was initially a very strong hard kick (oil on brine) at the OOWC, there is now a small reflection due to the residual oil leg contrast against the completely brine filled water-leg.
Note: Due to the velocity increase in the produced zone, there will be a small TWT shift of the reflection at the OOWC location.

## Slide 107: 4D Difference Signal for Sweep
OOWC
3D
Oil sand
Water sand
Shale
Shale
OWC
rise
POWC
4D
Produced
oil
POWC
OOWC
4D signal = Peak-Trough of approx. equal amplitude
'RFC DOUBLET'
Impedance
dReflectivity
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 108: 4D Difference Signal for Sweep (cont.)
OOWC
3D
Oil sand
Water sand
Shale
Shale
OWC
rise
POWC
4D
Produced
oil
Impedance
'Hilbert transform'
'90 deg phase shift'
'Quadrature'
'Coloured inversion'
'Sparse-spike inversion'
4D signal = Blue trough where swept
'SINGLE LOOP on pseudo-AI'
d Pseudo impedance
POWC
OOWC
Notes: In practice, the 4D difference is displayed as ‘pseudo impedance' = Runsum or quadrature.
This represents a layer focus of the 4D difference instead of the interface focus of reflectivity.
Displaying the Base − Monitor difference results in a blue trough over the interval where the HC’s have been replaced by brine.

## Slide 109: 4D Difference Signal for Sweep (cont.)
Impedance
dReflectivity
OOWC
Oil sand
Water sand
Shale
Shale
OWC
rise
POWC
Produced
oil
4D signal = Peak-Trough of approx. equal amplitude
'RFC DOUBLET'
d Pseudo impedance
POWC
OOWC
4D signal = Blue trough where swept
'SINGLE LOOP on pseudo-AI'
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 110: 4D interpretation workflow: Seismic volumes
Baseline
Monitor
Ideally input data should be
pseudo-impedance(quadrature) with
low impedance = trough
Baseline B
Monitor MT
Time alignment using cross-correlation (4D time shifts)
Difference = MT - B
Timeshift
Additional volumes that should be generated and looked at:
NdRMS
(signed RRR)
Timeshifts w/ hi-res gates
NdRMS
dRMS
NRMSDiff
(RRR)
Time-strain

## Slide 111: Standards—Post-Stack Processing
  Input Baseline and Monitor seismic volumes are quadrature/pseudo-impedance volumes with trough indicating soft impedances.
  Calculate D as difference MT − B, where MT is time-aligned monitor volume.
  Ensure processed Baseline, Monitor, aligned Monitor, Difference and Timeshift cubes are available.
  Calculate timeshifts by correlating Monitor data to Baseline. Examine and discuss timeshift volumes calculated with different gates (for example, 240, 120, 60 ms). Shorter gates will have greater resolution but larger noise.
  Derive global matching filter; apply filter if amplitude correction exceeds 2% or phase correction exceeds 10° at any frequency in seismic bandwidth.
  Create, inspect and discuss dRMS, NdRMS and RRR volumes and maps.
  Record window used for RMS calculations, preferably in volume/map names.
Post-stack Processing
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 112: Additional 4D QC Products: dRMS
What is polarity of 4D signal ?
Hardening?
or
Softening?
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 113: Additional 4D QC Products: dRMS (cont.)
dRMS= ARMS(Base) − ARMS(Monitor)
What is the polarity of the 4D signal?
Hardening?
or
Softening?
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 114: Additional 4D QC Products: NdRMS
2*[RMS(Base) − RMS(Monitor)]
[RMS(Base) + RMS(Monitor)]
NdRMS =
NdRMS identifies problems related to incorrect shot/recvr scalars.
NdRMS shows that the problems of the undershoot persist to reservoir level.
Hardening
Softening
Hardening
Softening
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 115
4D Amplitude difference and dRMS
Monitor – Baseline Amplitude Difference
Hardening?
Softening?
Monitor-baseline difference

## Slide 116
4D Amplitude difference and dRMS
Monitor – Baseline Amplitude Difference
dRMS (100-ft gate)
Hardening
Softening
Hardening?
Softening?
Monitor-baseline difference

## Slide 117: Time-shift and Time-strain
where
t = fast time (recording time)
𝝉 = slow time (e.g., time of base survey, monitor survey)

## Slide 118: Time-shift and Time-strain
  Monitor arrives later than base: Time-Shift = negative.
  Time-Shift linked to average velocity change from surface.
  Time-Strain highlights changes within an interval – derivative of Time-Shift. Also correlated with velocity change.
Time-shift Time-strain
– 0 +
Monitor
Base
– 0 +

## Slide 119: Example of timeshifts and Timestrains:
Monitor later
Monitor sooner
-7 ms
+7 ms
TimeShift Cube
TimeStrain Cube
-5 %
+5 %
V decrease
V increase

## Slide 120: Example of timeshifts and Timestrains:
Monitor later
Monitor sooner
-7 ms
+7 ms
Timeshift Cube
Timestrain Cube
Difference cube (M-B)
Softening
Hardening
dRMS cube =RMS(B)-RMS(M), 40 ms gate
-5 %
+5 %
V decrease
V increase

## Slide 121
4D Standards

## Slide 122
Jan Stammeijer, Paul Hatchell
The Leading Edge, February 2014

## Slide 123: Standards—Attributes
Use 'intuitive' colour scales when displaying 4D attribute maps. Make sure to annotate hardening versus softening.
Extract attributes both from a 4D diff cube and as a difference between 3D maps extracted from base and monitor.
Any 4D result should preserve the sign of change. Start with DRMS = RMS(Base) − RMS(Monitor); which is appropriate for soft sands. (Change the polarity when sands are hard)
Connected volume analysis should only use (pseudo) impedance data as input.
When displaying 'normalized' attributes, specify how these have been calculated.
A minimum 4D interpretation suite contains at least a signed 4D amplitude map of the reservoir(s) and a 4D timeshift map at Top Reservoir.
4D Interpretation and Attributes
Notes: On a 4D Difference section, we observe a Positive − Negative reflection pair (Peak − Trough)
For a Monitor − Base (not everywhere the standard!).
This is irrespective of the Sst being harder or softer than the Shl!
All the other reflections have to be subtracted out (ideally).

## Slide 124
4D General

## Slide 125: (un) knowns – (un)knowns (Johnston, 2013)
Known knowns: we know we know
Knowns unknowns: we know that we do not know
Unknown knowns: we do not know we know (perhaps we forgot)
Unknowns unknowns: we do not know we do not know … those are the real surprises (Johnston: “Most 4D surveys contain at least one surprise.”)

## Slide 126: Readings/Background
Johnston, David H, 2013. Practical Applications of Time-Lapse Seismic Data, Distinguished Instructor Short Course (DISC), Distinguished Instructor Series No.16, Society of Exploration Geophysicists
Hatchell, Paul, 2015. Youtube: https://www.youtube.com/watch?v=1jm70tZ8liE Experience with Time-Lapse Monitoring, European Association of Geoscientists & Engineers (EAGE)

## Slide 127: Exercise/Demo on Sleipner, 3 vintages (base + 2 monitor surveys) using Jupyter Notebooks (Python)

## Slide 128
2 x 3D 4D and 4D > 3D
Monitoring is measuring meaningful production related changes through time so we better can understand and manage our fields.
4D is measuring changes spatially across a field through time.
Time lapse is measuring changes through time
1D, 2D or 3D.
What is 4D ?

## Slide 129
Premise
or
?

## Slide 130
Little details we cannot see can make a difference

## Slide 131: Relate cores to logs

## Slide 132: Causes of changes
Differences in processing (cont’d)
Test 1990’s (Les Hatton):
Same dataset delivered to main contractors
Result:
many different sections with large
differences
(sometimes even polarity changes)
- Software contained at least 3 to 5
errors per 1000 lines of code

## Slide 133: Confirmation petro-elastic model with seismic

## Slide 134: Time-STRAIN Attribute:
Time strain is derivative of timeshift and is dimensionless:
TimeStrain(t) = 100 * [ TimeShift (t+dt) – TimeShift(t-dt) ] /(2*dt)
Note:
Factor of 100 allows this to be displayed on same scale as time shifts